## Slide 1: Cisco Routers
Presented By
Dr. Waleed Alseat
Mutah University

## Slide 2: Cisco Routers models

## Slide 3: How to choose the appropriate Cisco router
http://www.cisco.com/en/US/products/hw/routers/

## Slide 4: Router Initialization

## Slide 5: Router components
Router is typically like a computer which operates with
Two main components
  Hardware (Router physical components )
  Software (IOS)
    Internetworking operating system.
    configuration file

## Slide 6: Router hardware components
Power Supply
CPU
Memory (RAM , NVRAM ,ROM ,Flash )
System bus
Interfaces

## Slide 7: Router physical characteristics

## Slide 8: Router external connections

## Slide 9: Ports and Interfaces
Port - normally means one of the management ports used for administrative access
Interface normally refers to interfaces that are capable of sending and receiving user traffic.
Note: However, these terms are often used interchangeably in the industry and even with IOS output.

## Slide 10: Management Ports
Console port - Most common of the management ports
  Used to connect a terminal,
  Or most likely a PC running terminal emulator software,
No need for network access to that router.
The console port must be used during initial configuration of the router.
Auxiliary (AUX) port
Not all routers have auxiliary ports.
  At times, can be used similarly to a console port
  Can also be used to attach a modem.
Note: Auxiliary ports will not be used in this curriculum.

## Slide 11: Router Interfaces
Interface on Cisco routers refers to a physical connector on the router whose main purpose is to receive and forward packets.
Routers have multiple interfaces used to connect to multiple networks which may mean:
  Various types of networks
  Different types of media and connectors.
  Different types of interfaces.
For example, Fast Ethernet interfaces for connections to different LANs and also have different types of WAN interfaces used to connect a variety of serial links, including T1, DSL, and ISDN.

## Slide 12: Router Interfaces
Every interface on the router:
  Belongs to a different network
Cisco IOS will not allow two active interfaces on the same router to belong to the same network.

## Slide 13: LAN Interfaces
Ethernet and Fast Ethernet interfaces.
Used to connect the router to the LAN, similar to how a PC’s Ethernet NIC.
  Layer 2 MAC address
  Participates in the Ethernet LAN the same way as any other hosts on that LAN.
    Example: Address Resolution Protocol (ARP):
      Maintains ARP cache for that interface
      Sends ARP requests when needed
      Responds with ARP replies when required
Typically an RJ-45 jack (UTP).
  Router to switch: straight-through cable.
  Router to router via Ethernet interfaces, or PC’s NIC to router’s Ethernet interface: crossover cable.

## Slide 14: WAN Interfaces
Example: serial, ISDN, and Frame Relay interfaces.
Used to connect routers to external networks, usually over a larger geographical distance.
The Layer 2 encapsulation can be different types including:
  PPP
  Frame Relay
  HDLC (High-Level Data Link Control).
Similar to LAN interfaces, each WAN interface has its own IP address and subnet mask, making it a member of a specific network.
Note: MAC addresses are used only on Ethernet interfaces and are not on WAN interfaces.
However, WAN interfaces use their own Layer 2 addresses depending on the technology.
Layer 2 WAN encapsulation types and addresses are covered later in the course.

## Slide 15: Serial Connectors
Cisco routers support the EIA/TIA-232, EIA/TIA-449, V.35, X.21, and EIA/TIA-530 standards for serial connections,
Memorizing these connection types is not important.
Just know that a router has a DB-60 port that can support five different cabling standards.

## Slide 16: Serial Connectors
Router is typically a DTE device.
The DTE cable is connected to the serial interface on the router to a CSU/DSU device (DCE).
DTE Cable
DCE Cable

## Slide 17: Physically Connecting a WAN Interface
Typically, the router is the DTE device and is connected to a CSU/DSU, which is the DCE device.
  Serial interfaces require a clock signal to control the timing of the communications.
  In most environments, the service provider (a DCE device such as a CSU/DSU) will provide the clock.
  By default, Cisco routers are DTE devices

## Slide 18: Serial Connectors
In our labs we will use serial DTE/DCE cables (no CSU/DSU) with a DTE cable connected to one router and a DCE cable connected to the other router.

## Slide 19: Ethernet Connectors
Straight-through cables are used for:
  Switch-to-router
  Hub-to-router
  Switch-to-PC/server
  Hub-to-PC/server
Crossover cables are used for:
  Switch-to-switch
  PC/server-to-PC/server
  Switch-to-hub
  Hub-to-hub
  Router-to-router
  Router-to-PC/server

## Slide 20: Cisco Software components
Cisco IOS (Internetwork Operating System)
  It is the operating system that manages the hardware
  platform it is working on.
Configuration File
  It is a program file that contains commands that
  reflect how the router will react.